# e3an Multiple Choice Question Template

http://www.ecs.soton.ac.uk/e3an/Templates/e3an_mcq.dot

| Question Identifier | SJW29 | Item | 1 | of | 1 |
| --- | --- | --- | --- | --- | --- |

The Question

Question Stem

A second-order low pass Butterworth filter has normalised transfer function Using the Bilinear transformation, obtain the transfer function of a high pass digital Butterworth filter given a sampling rate of 8kHz and a cutoff frequency of 1.6kHz.

Copy of Graphic for question

Picture File for question (e.g. DavisHC05PIC1.gif)

Possible Answers (Note that generally an MCQ should have 5 possible answers)

Answer A (which may be/include a picture)

Picture File for Answer A (Either as whole answer or as well as text above) (e.g. DavisHC05PIC2.gif)

Feedback A

Answer B (which may be/include a picture)

Picture File B (e.g. DavisHC05PIC3.gif)

Feedback B

You have designed a LOW PASS filter.

Answer C (which may be/include a picture)

Picture File C

Feedback C

Correct

Answer D (which may be/include a picture)

Picture File D

Feedback D

You may have forgotten to pre-warp the cutoff frequency

Answer E (which may be/include a picture)

Picture File E

Feedback E

Answer F (which may be/include a picture)

Picture File F

Feedback F

### The Answer

| What is the Correct Answer? (A-F) | C |
| --- | --- |
| Can the order of the answers be randomised? (Yes/No) | Yes |

Notes for Tutors on Question (Working for answer etc.)

Pre-warping The required low pass to high pass frequency transformation is Giving a de-normalised transfer function Using the Bilinear transformation

Picture File used in notes (e.g. scanned worked answer) (e.g. DavisHC05PIC8.gif)